## Slide 1: Chapter 13 Embedded Operating Systems
Ninth Edition By William Stallings
Operating Systems: Internals and Design Principles
Notes: “Operating Systems: Internal and Design Principles”, 9/e, by William Stallings, Chapter 13 “Embedded Operating Systems”.

## Slide 2: Embedded System
The term embedded system refers to the use of electronics and software within a product that has a specific function or set of functions, as opposed to a general-purpose computer
An embedded system can also be defined as any device that includes a computer chip, but that is not a general-purpose workstation, or desktop or laptop computer
Examples of types of devices with embedded systems include cell phones, digital cameras, video cameras, calculators, home security systems, washing machines, various automotive systems, tennis rackets, toothbrushes, and numerous types of sensors and actuators in automated systems
Notes: The term embedded system refers to the use of electronics and software within a
product that has a specific function or set of functions, as opposed to a general-purpose
computer, such as a laptop or desktop system. We can also define an
embedded system as any device that includes a computer chip, but that is not a
general-purpose workstation, or desktop or laptop computer. Hundreds of millions
of computers are sold every year, including laptops, personal computers, workstations,
servers, mainframes, and supercomputers. In contrast, tens of billions of
microcontrollers are produced each year that are embedded within larger devices.
Today, many, perhaps most devices that use electric power have an embedded computing
system. It is likely in the near future, virtually all such devices will have
embedded computing systems.
Types of devices with embedded systems are almost too numerous to list.
Examples include cell phones, digital cameras, video cameras, calculators,
microwave ovens, home security systems, washing machines, lighting systems, thermostats,
printers, various automotive systems (e.g., transmission control, cruise
control, fuel injection, anti-lock brakes, and suspension systems), tennis rackets,
toothbrushes, and numerous types of sensors and actuators in automated systems.

## Slide 3: Embedded System
Often, embedded systems are tightly coupled to their environment
This can give rise to real-time constraints imposed by the need to interact with the environment
Constraints, such as required speeds of motion, required precision of measurement, and required time durations, dictate the timing of software operations
If multiple activities must be managed simultaneously, this imposes more complex real-time constraints
Notes: Often, embedded systems are tightly coupled to their environment. This can give
rise to real-time constraints imposed by the need to interact with the environment.
Constraints, such as required speeds of motion, required precision of measurement,
and required time durations, dictate the timing of software operations. If multiple
activities must be managed simultaneously, this imposes more complex real-time
constraints.

## Slide 4
Notes: Figure 13.1 shows in general terms an embedded system organization. In addition
to the processor and memory, there are a number of elements that differ from
the typical desktop or laptop computer:
• There may be a variety of interfaces that enable the system to measure, manipulate,
and otherwise interact with the external environment. Embedded systems
often interact (sense, manipulate, and communicate) with the external world
through sensors and actuators, and hence are typically reactive systems; a reactive
system is in continual interaction with the environment and executes at a
pace determined by that environment.
• The human interface may be as simple as a flashing light or as complicated as
real-time robotic vision. In many cases, there is no human interface.
• The diagnostic port may be used for diagnosing the system that is being
controlled— not just for diagnosing the computer.
• Special-purpose field programmable (FPGA), application-specific (ASIC), or
even nondigital hardware may be used to increase performance or reliability.
• Software often has a fixed function and is specific to the application.
• Efficiency is of paramount importance for embedded systems. These systems
are optimized for energy, code size, execution time, weight and dimensions,
and cost.
There are several noteworthy areas of similarity to general-purpose computer
systems as well:
• Even with nominally fixed function software, the ability to field upgrade to fix
bugs, to improve security, and to add functionality have become very important
for embedded systems, and not just in consumer devices.
• One comparatively recent development has been of embedded system platforms
that support a wide variety of apps. Good examples of this are smartphones
and audio/visual devices, such as smart TVs.

## Slide 5: Application Processors vs Dedicated Processors
Application Processor
Defined by the processor’s ability to execute complex operating systems, such as Linux, Android, and Chrome
Is general purpose in nature
A good example of the use of an embedded application processor is the smartphone
    The embedded system is designed to support numerous apps and perform a wide variety of functions
Dedicated Processor
Dedicated to one or a small number of specific tasks required by the host device
Because such an embedded system is dedicated to a specific task or tasks, the processor and associated components can be engineered to reduce size and cost
Notes: Application processors are defined by the processor’s ability to execute complex
operating systems, such as Linux, Android, and Chrome. Thus, the application processor
is general purpose in nature. A good example of the use of an embedded
application processor is the smartphone. The embedded system is designed to support
numerous apps and perform a wide variety of functions.
Most embedded systems employ a dedicated processor, which, as the name
implies, is dedicated to one or a small number of specific tasks required by the
host device. Because such an embedded system is dedicated to a specific task or
tasks, the processor and associated components can be engineered to reduce size
and cost.

## Slide 6: Microprocessors
A microprocessor is a processor whose elements have been miniaturized into one or a few integrated circuits
Early microprocessor chips included registers, an arithmetic logic unit (ALU), and some sort of control unit or instruction processing logic
Contemporary microprocessor chips include multiple processors, called cores, and a substantial amount of cache memory
However, a microprocessor chip includes only some of the elements that make up a computer system
Notes: A microprocessor is a processor whose elements have been miniaturized into one
or a few integrated circuits. Early microprocessor chips included registers, an arithmetic
logic unit (ALU), and some sort of control unit or instruction processing logic.
As transistor density increased, it became possible to increase the complexity of
the instruction set architecture, and ultimately to add memory and more than one
processor. Contemporary microprocessor chips include multiple processors, called
cores, and a substantial amount of cache memory.

## Slide 7
Notes: As shown in Figure 13.2,
a microprocessor chip includes only some of the elements that make up a computer
system.

## Slide 8: Microprocessors
Printed circuit board (PCB)
    A rigid, flat board that holds and interconnects chips and other electronic components
    Is made up of layers, typically two to ten, that interconnect components via copper pathways that are etched into the board
Motherboard
    The main PCB in a computer
    Also called a system board
Expansion board
    Smaller PCB that plugs into the slots in the main board
Chip
    Most prominent element on the motherboard
    A single piece of semiconducting material, typically silicon, upon which electronic circuits and logic gates are fabricated
    The resulting product is referred to as an integrated circuit
Multicore processor
    The motherboard contains a slot or socket for the processor chip, which typically contains multiple individual cores, in what is known as a multicore processor
Notes: Most computers, including embedded computers in smartphones and tablets, as
well as personal computers, laptops, and workstations, are housed on a motherboard.
Before describing this arrangement, we need to define some terms. A printed circuit
board (PCB) is a rigid, flat board that holds and interconnects chips and other electronic
components. The board is made of layers, typically two to ten, that interconnect
components via copper pathways that are etched into the board. The main PCB in a
computer is called a system board or motherboard , while smaller ones that plug into
the slots in the main board are called expansion boards.
The most prominent elements on the motherboard are the chips. A chip is a single
piece of semiconducting material, typically silicon, upon which electronic circuits
and logic gates are fabricated. The resulting product is referred to as an integrated
circuit .
The motherboard contains a slot or socket for the processor chip, which typically
contains multiple individual cores, in what is known as a multicore processor .
There are also slots for memory chips, I/O controller chips, and other key computer
components. For desktop computers, expansion slots enable the inclusion of more
components on expansion boards. Thus, a modern motherboard connects only a few
individual chip components, with each chip containing from a few thousand up to
hundreds of millions of transistors.

## Slide 9
Notes: A microcontroller is a single chip that contains the processor, nonvolatile memory
for the program (ROM or flash), volatile memory for input and output (RAM), a
clock, and an I/O control unit. It is also called a “computer on a chip.” A microcontroller
chip makes a substantially different use of the logic space available. Figure 13.3
shows in general terms the elements typically found on a microcontroller chip. The
processor portion of the microcontroller has a much lower silicon area than other
microprocessors and much higher energy efficiency.
Billions of microcontroller units are embedded each year in myriad products
from toys to appliances to automobiles. For example, a single vehicle can use 70
or more microcontrollers. Typically, especially for the smaller, less-expensive microcontrollers,
they are used as dedicated processors for specific tasks. For example,
microcontrollers are heavily utilized in automation processes. By providing simple
reactions to input, they can control machinery, turn fans on and off, open and close
valves, and so forth. They are integral parts of modern industrial technology and are
among the most inexpensive ways to produce machinery that can handle extremely
complex functionalities.
Microcontrollers come in a range of physical sizes and processing power. Processors
range from 4-bit to 32-bit architectures. Microcontrollers tend to be much
slower than microprocessors, typically operating in the MHz range rather than the
GHz speeds of microprocessors. Another typical feature of a microcontroller is that
it does not provide for human interaction. The microcontroller is programmed for a
specific task, embedded in its device, and executes as and when required.

## Slide 10: Deeply Embedded System
A deeply embedded system has a processor whose behavior is difficult to observe both by the programmer and the user
A deeply embedded system:
    Uses a microcontroller rather than a microprocessor
    Is not programmable once the program logic for the device has been burned into ROM (read only memory)
    Has no interaction with a user
    Deeply embedded systems are dedicated, single-purpose devices that detect something in the environment, perform a basic level of processing, then do something with the results
    They often have wireless capability and appear in networked configurations, such as networks of sensors deployed over a large area
    The Internet of Things depends heavily on deeply embedded systems
    Typically, deeply embedded systems have extreme resource constraints in terms of memory, processor size, time, and power consumption
Notes: A large percentage of the total number of embedded systems are referred to as
deeply embedded systems . Although this term is widely used in the technical and
commercial literature, you will search the Internet in vain (at least the writer did) for
a straightforward definition. Generally, we can say a deeply embedded system has
a processor whose behavior is difficult to observe both by the programmer and the
user. A deeply embedded system uses a microcontroller rather than a microprocessor,
is not programmable once the program logic for the device has been burned into
ROM (read-only memory), and has no interaction with a user.
Deeply embedded systems are dedicated, single-purpose devices that detect
something in the environment, perform a basic level of processing, then do something
with the results. Deeply embedded systems often have wireless capability
and appear in networked configurations, such as networks of sensors deployed
over a large area (e.g., factory, agricultural field). The Internet of Things depends
heavily on deeply embedded systems. Typically, deeply embedded systems have
extreme resource constraints in terms of memory, processor size, time, and power
consumption.

## Slide 11: Characteristics of Embedded OS
Real-time operation
Reactive operation
Configurability
I/O device flexibility
Streamlined protection mechanisms
Direct use of interrupts
Notes: A simple embedded system, with simple functionality, may be controlled by a
special-purpose program or set of programs with no other software. Typically,
more complex embedded systems include an OS. Although it is possible in
principle to use a general-purpose OS, such as Linux, for an embedded system,
constraints of memory space, power consumption, and real-time requirements
typically dictate the use of a special-purpose OS designed for the embedded
system environment.
The following are some of the unique characteristics and design requirements
for embedded operating systems:
• Real-time operation: In many embedded systems, the correctness of a computation
depends, in part, on the time at which it is delivered. Often, real-time
constraints are dictated by external I/O and control stability requirements.
• Reactive operation: Embedded software may execute in response to external
events. If these events do not occur periodically or at predictable intervals, the
embedded software may need to take into account worst-case conditions and
set priorities for execution of routines.
• Configurability: Because of the large variety of embedded systems, there is
a large variation in the requirements, both qualitative and quantitative, for
embedded OS functionality. Thus, an embedded OS intended for use on a
variety of embedded systems must lend itself to flexible configuration so that
only the functionality needed for a specific application and hardware suite is
provided. [MARW06] gives the following examples. The linking and loading
functions can be used to select only the necessary OS modules to load.
Conditional compilation can be used. If an object-oriented structure is used,
proper subclasses can be defined. However, verification is a potential problem
for designs with a large number of derived tailored operating systems.
Takada cites this as a potential problem for eCos [TAKA01].
• I/O device flexibility: There is virtually no device that needs to be supported
by all versions of the OS, and the range of I/O devices is large. [MARW06]
suggests that it makes sense to handle relatively slow devices such as disks and
network interfaces by using special tasks instead of integrating their drives into
the OS kernel.
Streamlined protection mechanisms: Embedded systems are typically designed
for a limited, well-defined functionality. Untested programs are rarely added
to the software. After the software has been configured and tested, it can be
assumed to be reliable. Thus, apart from security measures, embedded systems
have limited protection mechanisms. For example, I/O instructions need
not be privileged instructions that trap to the OS; tasks can directly perform
their own I/O. Similarly, memory protection mechanisms can be minimized.
[MARW06] provides the following example. Let switch correspond to the
memory-mapped I/O address of a value that needs to be checked as part of an
I/O operation. We can allow the I/O program to use an instruction such as load
register , switch to determine the current value. This approach is preferable
to the use of an OS service call, which would generate overhead for saving
and restoring the task context.
• Direct use of interrupts: General-purpose operating systems typically do not
permit any user process to use interrupts directly. [MARW06] lists three
reasons why it is possible to let interrupts directly start or stop tasks (e.g., by
storing the task’s start address in the interrupt vector address table) rather than
going through OS interrupt service routines: (1) Embedded systems can be
considered to be thoroughly tested, with infrequent modifications to the OS or
application code; (2) protection is not necessary, as discussed in the preceding
bullet item; and (3) efficient control over a variety of devices is required.

## Slide 12
Notes: A key differentiator between desktop/server and embedded Linux distributions is
that desktop and server software is typically compiled or configured on the platform
where it will execute, while embedded Linux distributions are usually compiled or
configured on one platform, called the host platform, but are intended to be executed
on another, called the target platform (see Figure 13.4). The key elements that are
developed on the host system and then transferred to the target system are the boot
loader, the kernel, and the root file system.

## Slide 13: Host and Target Environments
Boat loader
  A small program that calls the OS into memory (RAM) after the power is turned on
  It is responsible for the initial boot process of the system and for loading the kernel into main memory
Root file system
    Contains all the files needed for the system to work properly
    The root file system of an embedded OS is similar to that found on a workstation or server, except that it contains only the minimal set of application, libraries, and related files needed to run the system
Kernel
  The full kernel includes a number of separate modules including:
      Memory management
      Process/thread management
      Inter process communication, timers
      Device drivers for I/O, network, sound, storage, graphics, etc
      File systems
      Networking
      Power management
Notes: The boot loader is a small program that calls the OS into memory
(RAM) after the power is turned on. It is responsible for the initial boot process of
the system, and for loading the kernel into main memory. A typical sequence in an
embedded system is the following:
1. The processor in the embedded system executes code in ROM to load a first-stage
boot loader from internal flash memory, a Secure Digital (SD) card, or a
serial I/O port.
2. The first-stage boot loader initializes the memory controller and a few peripherals
and loads a second-stage boot loader into RAM. No interaction is possible
with this boot loader, and it is typically provided by the processor vendor
on ROM.
3. The second-stage boot loader loads the kernel and root file system from flash
memory to main memory (RAM). The kernel and the root file system are generally
stored in flash memory in compressed files, so part of the book loading
process is to decompress the files into binary images of the kernel and root file
system. The boot loader then passes control to the kernel. Typically, an open-source
boot loader is used for the second stage.
The full kernel includes a number of separate modules, including:
• Memory management.
• Process/thread management.
• Inter process communication, timers.
• Device drivers for I/O, network, sound, storage, graphics, etc.
• File systems.
• Networking.
• Power management.
From the full kernel software for a given OS, a number of optional components
will be left out for an embedded system. For example, if the embedded system
hardware does not support paging, then the memory management subsystem can be
eliminated. The full kernel will include multiple file systems, device drivers, and so
on, and only a few of these may be needed.
In an embedded OS, or any OS, a global single hierarchy of
directories and files is used to represent all the files in the system. At the top, or
root of this hierarchy is the root file system, which contains all the files needed for
the system to work properly. The root file system of an embedded OS is similar to
that found on a workstation or server, except that it contains only the minimal set of
applications, libraries, and related files needed to run the system.
In an embedded OS, or any OS, a global single hierarchy of
directories and files is used to represent all the files in the system. At the top, or
root of this hierarchy is the root file system, which contains all the files needed for
the system to work properly. The root file system of an embedded OS is similar to
that found on a workstation or server, except that it contains only the minimal set of
applications, libraries, and related files needed to run the system.

## Slide 14
Notes: A key differentiator between desktop/server and embedded Linux distributions
is that desktop and server software is typically compiled on the platform where it will
execute, while embedded Linux distributions are usually compiled on one platform
but are intended to be executed on another. The software used for this purpose is
referred to as a cross-compiler . Figure 13.5 illustrates its use.

## Slide 15: Developing an Embedded OS
Two general approaches:
Take an existing OS and adapt it for the embedded application
Design and implement an OS intended solely for embedded use
Notes: There are two general approaches to developing an embedded OS.
  The first approach is to take an existing OS and adapt it for the embedded application.
  The other approach is to design and implement an OS intended solely for embedded use

## Slide 16: Adapting an Existing OS
An existing commercial OS can be used for an embedded system by adding:
    Real time capability
    Streamlining operation
    Adding necessary functionality
Advantage:
Familiar interface
Disadvantage:
Not optimized for real-time and embedded applications
Notes: An existing commercial OS can be used for an embedded system by adding real time
capability, streamlining operation, and adding necessary functionality. This
approach typically makes use of Linux, but FreeBSD, Windows, and other general purpose
operating systems have also been used. Such operating systems are typically
slower and less predictable than a special-purpose embedded OS. An advantage of
this approach is that the embedded OS derived from a commercial general-purpose
OS is based on a set of familiar interfaces, which facilitates portability.
The disadvantage of using a general-purpose OS is that it is not optimized
for real-time and embedded applications. Thus, considerable modification may be
required to achieve adequate performance. In particular, a typical OS optimizes for
the average case rather than the worst case for scheduling, usually assigns resources
on demand, and ignores most if not all semantic information about an application.

## Slide 17: Purpose-Built Embedded OS
Typical characteristics include:
  Fast and lightweight process or thread switch
  Scheduling policy is real time and dispatcher module is part of scheduler
  Small size
  Responds to external interrupts quickly
  Minimizes intervals during which interrupts are disabled
  Provides fixed or variable-sized partitions for memory management
  Provides special sequential files that can accumulate data at a fast rate
Notes: A significant number of operating systems have been designed from the ground up
for embedded applications. Two prominent examples of this latter approach are
eCos and TinyOS, both of which are discussed in this chapter.
Typical characteristics of a specialized embedded OS include the following:
• Has a fast and lightweight process or thread switch
• Scheduling policy is real time and dispatcher module is part of scheduler
instead of separate component.
• Has a small size
• Responds to external interrupts quickly; typical requirement is response time
of less than 10 μs
• Minimizes intervals during which interrupts are disabled
• Provides fixed or variable-sized partitions for memory management as well as
the ability to lock code and data in memory
• Provides special sequential files that can accumulate data at a fast rate

## Slide 18: Timing Constraints
To deal with timing constraints, the kernel:
Provides bounded execution time for primitives
Maintains a real-time clock
Provides for special alarms and timeouts
Supports real-time queuing disciplines
Provides primitives to delay processing by a fixed amount of time and to suspend/resume execution
Notes: To deal with timing constraints, the kernel
• Provides bounded execution time for most primitives
• Maintains a real-time clock
Provides for special alarms and time-outs
• Supports real-time queuing disciplines such as earliest deadline first and
primitives for jamming a message into the front of a queue
• Provides primitives to delay processing by a fixed amount of time and to
suspend/resume execution
The characteristics just listed are common in embedded operating systems with
real-time requirements. However, for complex embedded systems, the requirement
may emphasize predictable operation over fast operation, necessitating different
design decisions, particularly in the area of task scheduling.

## Slide 19: Embedded Linux
A version of Linux running in an embedded system
Embedded devices typically require support for a specific set of devices, periphrals, and protocols, depending on the hardware that is present in a given device and the intended purpose of that device
An embedded Linux distribution is a version of Linux to be customized for the size and hardware constraints of embedded devices
    Includes software packages that support a variety of services and applications on those devices
    An embedded Linux kernel will be far smaller than an ordinary Linux kernel
Notes: The term embedded Linux simply means a version of Linux running in an embedded
system. Typically, an embedded Linux system uses one of the official kernel
releases, although some systems use a modified kernel tailored to a specific hardware
configuration or to support a certain class of applications. Primarily, an embedded
Linux kernel differs from a Linux kernel used on a workstation or server by the build
configuration and development framework.
Desktop and server Linux systems need to support a large number of devices because
of the wide variety of configurations that use Linux. Similarly, such systems
also need to support a range of communication and data exchange protocols so that
they can be used for a large number of different purposes. Embedded devices typically
require support for a specific set of devices, peripherals, and protocols, depending
on the hardware that is present in a given device and the intended purpose of
that device. Fortunately, the Linux kernel is highly configurable in terms of the architecture
that it is compiled for and the processors and devices that it supports.
An embedded Linux distribution is a version of Linux to be customized for
the size and hardware constraints of embedded devices, and includes software packages
that support a variety of services and applications on those devices. Thus, an
embedded Linux kernel will be far smaller than an ordinary Linux kernel.

## Slide 20
Notes: [ETUT16] classifies the size of an embedded Linux system by the
amount of available ROM and RAM, using the three broad categories of small,
medium, and large. Small systems are characterized by a low-powered processor
with a minimum of 2 MB of ROM and 4 MB of RAM. Medium-sized systems
are characterized by a medium-powered processor with around 32 MB of ROM
and 64 MB of RAM. Large systems are characterized by a powerful processor or
collection of processors combined with large amounts of RAM and permanent
storage.
On a system without permanent storage, the entire Linux kernel must fit in
the RAM and ROM. A full-featured modern Linux system would not do so. As an
indication of this, Figure 13.6 shows the compressed size of the full Linux kernel as it
has grown over time. Of course, any Linux system will be configured with only some
of the components of the full release. Even so, this chart gives an indication of the
fact that substantial amounts of the kernel must be left out, especially for small and
medium-sized embedded systems.

## Slide 21
Description | Type | Size | Time constraints | Networkability | Degree of user interaction
Accelerator control devices | Industrial process control | Medium | Stringent | Yes | Low
Computer-aided training system | Aerospace | Large | Stringent | No | High
Bluetooth device for accessing local information | Networking | Small | Mild | Yes | Very low
System control and data acquisition protocol converter | Industrial process control | Medium | Stringent | No | Very low
Personal digital assistant | Consumer electronics | Medium | Mild | Yes | Very high
Motor control device involved with space vehicle control | Aerospace | Large | Stringent | Yes | High
Table 13.1
Characteristics of Example Embedded Linux Systems
(Table is on page 583 in the textbook)
Notes: Other characteristics of embedded Linux systems
include:
• Time constraints: Stringent time constraints require the system to respond in
a specified time period. Mild time constraints are appropriate for systems in
which timely response is not critical.
• Networkability: Networkability refers to whether a system can be connected to
a network. Virtually all embedded devices today have this capability, typically
wireless.
• Degree of user interaction: Some devices are centered on user interaction, such
as smartphones. Other devices, such as industrial process control, might provide
a very simple interface, such as LEDs and buttons for interaction. And other
devices have no end user interaction, such as IoT sensors that gather information
and transmit them to a cloud.
Table 13.1, from [ETUT16], gives characteristics of some commercially available
embedded systems using a Linux kernel.

## Slide 22: Embedded Linux File Systems
File system must be as small as possible
Commonly used examples:
  cramfs
      A simple read-only file system that is designed to minimize size by maximizing the efficient use of underlying storage
      Files are compressed in units that match the Linux page size
  squashfs
      A compressed, read-only file system that was designed for use on low memory or limited storage size environments
  jffs2
      A log-based file system that is designed for use on NOR and NAND flash devices with special attention to flash-oriented issues such as wear-leveling
  ubifs
      Provides better performance on larger flash devices and also supports write caching to provide additional performance inprovements
  yaffs2
      Provides a fast and robust file system for large flash devices
Notes: Some applications may create relatively small file systems to be used only for the duration
of the application and which can be stored in main memory. But in general, a
file system must be stored in persistent memory, such as flash memory or traditional
disk-based storage devices. For most embedded systems, an internal or external disk
is not an option, and persistent storage is generally provided by flash memory.
As with other aspects of an embedded Linux system, the file system must be as
small as possible. A number of such compact file systems have been designed for use
in embedded systems. The following are commonly used examples:
• cramfs: The Compressed RAM file system is a simple read-only file system
that is designed to minimize size by maximizing the efficient use of underlying
storage. Files on cramfs file systems are compressed in units that match the
Linux page size (typically 4096 bytes or 4 MB, based on kernel version and
configuration) to provide efficient random access to file contents.
• squashfs: Like cramfs, squashfs is a compressed, read-only file system that was
designed for use on low memory or limited storage size environments such as
embedded Linux systems.
• jffs2: The Journaling Flash File System, version 2, is a log-based file system
that, as the name suggests, is designed for use on NOR and NAND flash devices
with special attention to flash-oriented issues such as wear-leveling.
• ubifs: The Unsorted Block Image File System generally provides better performance
than jffs2 on larger flash devices, and also supports write caching to
provide additional performance improvements.
• yaffs2: Yet another Flash File System, version 2, provides a fast and robust file
system for large flash devices. Yaffs2 requires less RAM to hold file system
state information than file systems such as jffs2, and also generally provides
better performance if the file system is being written to frequently.

## Slide 23: Advantages of Embedded Linux
Advantages of using Linux as the basis for an embedded OS include the following:
  Vendor independence
    The platform provider is not dependent on a particular vendor to provide needed features and meet deadlines for deployment
  Varied hardware support
    Linux support for a wide range of processor architectures and peripheral devices makes it suitable for virtually any embedded system
  Low cost
    The use of Linux minimizes cost for development and training
  Open source
    The use of Linux provides all of the advantages of open source software
Notes: Embedded versions of Linux began to appear as early as 1999. A number of companies
have developed their own versions tailored to specific platforms. Advantages of
using Linux as the basis for an embedded OS include the following:
• Vendor independence: The platform provider is not dependent on a particular
vendor to provide needed features and meet deadlines for deployment.
• Varied hardware support: Linux support for a wide range of processor architectures
and peripheral devices makes it suitable for virtually any embedded
system.
• Low cost: The use of Linux minimizes cost for development and training.
• Open source: The use of Linux provides all of the advantages of open source
software.

## Slide 24: 𝜇Clinux
𝜇Clinux (microcontroller Linux) is a popular open-source Linux kernel variation targeted at microcontrollers and other very small embedded systems
The design philosophy for 𝜇Clinux is to slim down the operating environment by removing utility programs, tools, and other system services that are not needed in an embedded environment
Notes: 𝜇Clinux (microcontroller Linux) is a popular open-source Linux kernel variation
targeted at microcontrollers and other very small embedded systems. Because of
the modular nature of Linux, it is easy to slim down the operating environment by
removing utility programs, tools, and other system services that are not needed in an
embedded environment. This is the design philosophy for 𝜇Clinux.
To get some feel for the size of a 𝜇Clinux bootable image (kernel plus root file
system), we look at the experience of EmCraft Systems, which builds board-level
systems using Cortex-M microcontrollers and Cortex-A microprocessors [EMCR15].
These are by no means the smallest embedded systems that use 𝜇Clinux. A minimal
configuration could be as little as 0.5 MB, but the vendor found the size of a practical
bootable image, with Ethernet, TCP/IP and a reasonable set of user space tools
and applications configured, would be in the range of 1.5 to 2 MB. The size of RAM
required for run-time 𝜇Clinux operation would be in the range of 8 to 32 MB. These
numbers are dramatically smaller than those of a typical Linux system.

## Slide 25: Differences Between 𝜇Clinux and Linux
Linux is a multiuser OS based on Unix. 𝜇Clinux is a version of Linux intended for embedded systems typically with no interactive user
Unlike Linux, 𝜇Clinux does not support memory management
The Linux kernel maintains a separate virtual address space for each process. 𝜇Clinux has a single shared address space for all processes
𝜇Clinux modifies device drivers to use the local system bus rather than ISA or PCI
In Linux, address space is recovered on context switching; this is not done in 𝜇Clinux
Unlike Linux, 𝜇Clinux does not provide the fork system call; the only option is to use vfork
The most significant difference between full Linux and 𝜇Clinux is in the area of memory management
Notes: Key differences between 𝜇Clinux and Linux for
larger systems include the following (see [MCCU04] for a further discussion):
• Linux is a multiuser OS based on UNIX. 𝜇Clinux is a version of Linux intended
for embedded systems typically with no interactive user.
• Unlike Linux, 𝜇Clinux does not support memory management. Thus, with
𝜇Clinux there are no virtual address spaces; applications must be linked to
absolute addresses.
• The Linux kernel maintains a separate virtual address space for each process.
𝜇Clinux has a single shared address space for all processes.
• In Linux, address space is recovered on context switching; this is not done in
𝜇Clinux
• Unlike Linux, 𝜇Clinux does not provide the fork system call; the only option
is to use vfork. The fork call essentially makes a duplicate of the calling process,
identical in almost every way (not everything is copied over, for example,
resource limits in some implementations, but the idea is to create as close a
copy as possible). The new process (child) gets a different process ID (PID)
and has the PID of the old process (parent) as its parent PID (PPID). The basic
difference between vfork and fork is that when a new process is created with
vfork, the parent process is temporarily suspended, and the child process might
borrow the parent’s address space. This continues until the child process either
exits, or calls execve, at which point the parent process continues.
• 𝜇Clinux modifies device drivers to use the local system bus rather than ISA
or PCI.
The most significant difference between full Linux and 𝜇Clinux is in the area
of memory management. The lack of memory management support in 𝜇Clinux has
a number of implications, including:
• The main memory allocated to a process must generally be contiguous. If a
number of processes swap in and out of memory, this can lead to fragmentation
(see Figure 7.4). However, embedded systems typically have a fixed set of
processes that are loaded at boot up time and continue until the next reset, so
this feature is generally not needed.
• 𝜇Clinux cannot expand memory for running process, because there may be
other processes contiguous to it. Thus, the brk and sbrk calls (dynamically
change the amount of space allocated for the data segment of the calling process)
are not available. But 𝜇Clinux does provide an implementation of malloc,
which is used to allocate a block of memory from a global memory pool.
• 𝜇Clinux lacks a dynamic application stack. This can result in a stack overflow,
which will corrupt memory. Care must be taken in application development and
configuration to avoid this.
• 𝜇Clinux does not provide memory protection, which presents the risk of an
application corrupting part of another application or even the kernel. Some
implementations do provide a fix for this. For example, the Cortex-M3/M4
architecture provides a memory protection mechanism called MPU (Memory
Protection Unit). Using the MPU, Emcraft Systems has added to the kernel
an optional feature that implements process-to-process and process-to-kernel
protection on par with the memory protection mechanisms implemented in
Linux using MMU [KHUS12].

## Slide 26
glibc name | glibc size | µçlibc name | µclibc size
libc-2.3.2.so | 1.2M | libuClibc-0.9.2.7.so | 284K
ld-2.3.2.so | 92K | libcrypt-0.9.2.7.so | 20K
libcrypt-2.3.2.so | 20K | libdl-0.9.2.7.so | 12K
libdl-2.3.2.so | 12K | libm-0.9.2.7.so | 8K
libm-2.3.2.so | 136K | libnsl-0.9.2.7so | 56K
libnsl-2.3.2.so | 76K | libpthread-0.9.2.7.so | 4K
libpthread-2.3.2.so | 84K | libresolv-0.9.2.7.so | 84K
libresolv-2.3.2.so | 68K | libutil-0.9.2.7.so | 4K
libutil-2.3.2.so | 8K | libcrypt-0.9.2.7.so | 8K
(Table is on page 586 in the textbook)
Table 13.2
Size of Some Functions in GNU C Library and µClibc
Notes: 𝜇Clibc is a C system library originally developed to support 𝜇Clinux and it
generally used in conjunction with 𝜇Clinux. However, 𝜇Clibc can also be used with
other Linux kernels. The main objective for 𝜇Clibc is to provide a system library that
is to provide a C library suitable for developing embedded Linux system. It is much
smaller than the GNU C Library, which is widely used on Linux systems, but nearly all
applications supported by glibc also work perfectly with 𝜇Clibc. Porting applications
from glibc to 𝜇Clibc typically involves just recompiling the source code. 𝜇Clibc even
supports shared libraries and threading.
Table 13.2, based on [ANDE05], compares the sizes of functions in the two
libraries. As can be seen, the space savings are considerable. These savings are
achieved by disabling some features by default and aggressively rewriting the code
to eliminate redundancy.

## Slide 27
Notes: Figure 13.7 shows the top-level software architecture of an embedded system
using 𝜇 Clinux and 𝜇 Clibc.

## Slide 28: Android
Focus of Android lies in the vertical integration of the Linux kernel and the Android user-space components
Many embedded Linux developers do not consider Android to be an instance of embedded Linux
  From the point of view of these developers, a classic embedded device has a fixed function, frozen at the factory
Android
More of a platform OS that can support a variety of applications that vary from one platform to the next
A vertically integrated system, including some Android specific modifications to the Linux kernel
An embedded OS based on a Linux kernel
Notes: As we have discussed throughout this book, Android is an embedded OS based on
a Linux kernel. Thus, it is reasonable to consider Android an example of embedded
Linux. However, many embedded Linux developers do not consider Android to be
an instance of embedded Linux [CLAR13]. From the point of view of these developers,
a classic embedded device has a fixed function, frozen at the factory. Android
is more of a platform OS that can support a variety of applications that vary from
one platform to the next. Further, Android is a vertically integrated system, including
some Android-specific modifications to the Linux kernel. The focus of Android
lies in the vertical integration of the Linux kernel and the Android user-space components.
Ultimately, it is a matter of semantics, with no “official” definition of embedded
Linux on which to rely.

## Slide 29: TinyOS
Streamlines to a very minimal OS for embedded systems
Core OS requires 400 bytes of code and data memory combined
Not a real-time OS
There is no kernel
There are no processes
OS doesn’t have a memory allocation system
Interrupt and exception handling is dependent on the peripheral
It is completely nonblocking, so there are few explicit synchronization primitives
Has become a popular approach to implementing wireless sensor network software
Notes: TinyOS provides a more streamlined approach for an embedded OS than
one based on a commercial general-purpose OS, such as an embedded version of
Linux. Thus, TinyOS and similar systems are better suited for small embedded systems
with tight requirements on memory, processing time, real-time response, power
consumption, and so on. TinyOS takes the process of streamlining to a much further
point, resulting in a very minimal OS for embedded systems. The core OS requires
400 bytes of code and data memory, combined.
TinyOS represents a significant departure from other embedded operating
systems. One striking difference is that TinyOS is not a real-time OS. The reason for
this is the expected workload, which is in the context of a wireless sensor network,
as described in the next subsection. Because of power consumption, these devices
are off most of the time. Applications tend to be simple, with processor contention
not much of an issue.
Additionally, in TinyOS there is no kernel, as there is no memory protection
and it is a component-based OS; there are no processes; the OS itself does not have
a memory allocation system (although some rarely used components do introduce
one); interrupt and exception handling is dependent on the peripheral; and it is
completely nonblocking, so there are few explicit synchronization primitives.
TinyOS has become a popular approach to implementing wireless sensor
network software. Currently, over 500 organizations are developing and contributing
to an open source standard for Tiny OS.

## Slide 30
Notes: TinyOS was developed primarily for use with networks of small wireless sensors. A
number of trends have enabled the development of extremely compact, low-power
sensors. The well-known Moore’s law continues to drive down the size of memory
and processing logic elements. Smaller size in turn reduces power consumption. Low
power and small size trends are also evident in wireless communications hardware,
micro-electromechanical sensors (MEMS), and transducers. As a result, it is possible
to develop an entire sensor complete with logic in a cubic millimeter. The application
and system software must be compact enough that sensing, communication, and computation
capabilities can be incorporated into a complete, but tiny, architecture.
Low–cost, small–size, low-power-consuming wireless sensors can be used in a
host of applications [ROME04]. Figure 13.8 shows a typical configuration. A base
station connects the sensor network to a host PC and passes on sensor data from the
network to the host PC, which can do data analysis and/or transmit the data over
a corporate network or Internet to an analysis server. Individual sensors collect
data and transmit these to the base station, either directly or through sensors that
act as data relays. Routing functionality is needed to determine how to relay the
data through the sensor network to the base station. [BUON01] points out that, in
many applications, the user will want to be able to quickly deploy a large number of
low-cost devices without having to configure or manage them. This means that they
must be capable of assembling themselves into an ad hoc network. The mobility of
individual sensors and the presence of RF interference means that the network will
have to be capable of reconfiguring itself in a matter of seconds.

## Slide 31: TinyOS Goals
With the tiny distributed sensor application in mind, the following goals were set for TinyOS:
  Allow high concurrency
  Operate with limited resources
  Adapt to hardware evolution
  Support a wide range of applications
  Support a diverse set of platforms
  Be robust
Notes: With the tiny, distributed sensor application in mind, a group of researchers from
UC Berkeley [HILL00] set the following goals for TinyOS:
• Allow high concurrency: In a typical wireless sensor network application, the
devices are concurrency intensive. Several different flows of data must be kept
moving simultaneously. While sensor data are input in a steady stream, processed
results must be transmitted in a steady stream. In addition, external
controls from remote sensors or base stations must be managed.
• Operate with limited resources: The target platform for TinyOS will have limited
memory and computational resources and run on batteries or solar power.
A single platform may offer only kilobytes of program memory and hundreds
of bytes of RAM. The software must make efficient use of the available processor
and memory resources while enabling low-power communication.
• Adapt to hardware evolution: Most hardware is in constant evolution; applications
and most system services must be portable across hardware generations.
Thus, it should be possible to upgrade the hardware with little or no software
change, if the functionality is the same.
• Support a wide range of applications: Applications exhibit a wide range of
requirements in terms of lifetime, communication, sensing, and so on. A modular,
general-purpose embedded OS is desired so that a standardized approach
leads to economies of scale in developing applications and support software.
• Support a diverse set of platforms: As with the preceding point, a general purpose
embedded OS is desirable.
• Be robust: Once deployed, a sensor network must run unattended for months
or years. Ideally, there should be redundancy both within a single system and
across the network of sensors. However, both types of redundancy require
additional resources. One software characteristic that can improve robustness
is to use highly modular, standardized software components.
It is worth elaborating on the concurrency requirement. In a typical application,
there will be dozens, hundreds, or even thousands of sensors networked
together. Usually, little buffering is done, because of latency issues. For example,
if you are sampling every 5 minutes and want to buffer four samples before sending,
the average latency is 10 minutes. Thus, information is typically captured, processed,
and streamed onto the network in a continuous flow. Further, if the sensor
sampling produces a significant amount of data, the limited memory space available
limits the number of samples that could be buffered. Even so, in some applications,
each of the flows may involve a large number of low-level events interleaved with
higher-level processing. Some of the high-level processing will extend over multiple
real-time events. Further, sensors in a network, because of the low power of transmission
available, typically operate over a short physical range. Thus data from outlying
sensors must be relayed to one or more base stations by intermediate nodes.

## Slide 32: TinyOS Components
Embedded software systems built with TinyOS consist of a set of modules (called components), each of which performs a simple task and which interface with each other and with hardware in limited and well-defined ways
The only other software module is the scheduler
Because there is no kernel there is no actual OS
The application area of interest is the wireless sensor network (WSN)
Examples of standardized components include:
Single-hop networking
Ad-hoc routing
Power management
Timers
Nonvolatile storage control
Notes: An embedded software system built using TinyOS consists of a set of small modules,
called components, each of which performs a simple task or set of tasks and which
interface with each other and with hardware in limited and well-defined ways. The
only other software module is the scheduler, discussed subsequently. In fact, because
there is no kernel, there is no actual OS. But we can take the following view. The application
area of interest is the wireless sensor network (WSN). To meet the demanding
software requirements of this application, a rigid, simplified software architecture
is dictated, consisting of components. The TinyOS development community has
implemented a number of open-source components that provide the basic functions
needed for the WSN application. Examples of such standardized components include
single-hop networking, ad-hoc routing, power management, timers, and nonvolatile
storage control. For specific configurations and applications, users build additional
special-purpose components and link and load all of the components needed for the
user’s application. TinyOS, then, consists of a suite of standardized components. Some
but not all of these components are used, together with application-specific user-written
components, for any given implementation. The OS for that implementation is simply
the set of standardized components from the TinyOS suite.

## Slide 33
Notes: All components in a TinyOS configuration have the same structure, an example
of which is shown in Figure 13.9a . The shaded box in the diagram indicates
the component, which is treated as an object that can only be accessed by defined
interfaces, indicated by white boxes. A component may be hardware or software.
Software components are implemented in nesC, which is an extension of C with
two distinguishing features: a programming model where components interact via
interfaces, and an event-based concurrency model with run-to-completion task and
interrupt handlers, explained subsequently.
The architecture consists of a layered arrangement of components. Each component
can link to only two other components, one below it in the hierarchy and one
above it. A component issues commands to its lower-level component and receives
event signals from it. Similarly, the component accepts commands from its upper-level
component and issues event signals to it. At the bottom of the hierarchy are hardware
components and at the top of the hierarchy are application components, which may
not be part of the standardized TinyOS suite but which must conform to the TinyOS
component structure.

## Slide 34: Components -- Tasks
A software component implements one or more tasks
Each task in a component is similar to a thread in an ordinary OS
Within a component tasks are atomic
    Once a task has started it runs to completion
A task cannot:
Be preempted by another task in the same component and there is no time slicing
Block or spin wait
A task can:
Perform computations
Call lower-level components (commands)
Signal higher-level events
Schedule other tasks
Notes: A software component implements one or more tasks. Each task in a component
is similar to a thread in an ordinary OS, with certain limitations. Within a component,
tasks are atomic: Once a task has started, it runs to completion. It cannot
be preempted by another task in the same component, and there is no time slicing.
However, a task can be preempted by an event. A task cannot block or spin wait.
These limitations greatly simplify the scheduling and management of tasks within
a component. There is only a single stack, assigned to the currently running task.
Tasks can perform computations, call lower-level components (commands) and signal
higher-level events, and schedule other tasks.

## Slide 35: Components -- Commands
A command is a nonblocking request
    A task that issues a command does not block or spin wait for a reply from the lower-level component
Is typically a request for the lower-level component to perform some service
The effect on the component that receives the command is specific to the command given and the task required to satisfy the command
A command cannot preempt the currently running task
A command does not cause a preemption in the called component and does not cause blocking in the calling component
Notes: Commands are nonblocking requests. That is, a task that issues a command
does not block or spin wait for a reply from the lower-level component. A command
is typically a request for the lower-level component to perform some service,
such as initiating a sensor reading. The effect on the component that receives the
command is specific to the command given and the task required to satisfy the command.
Generally, when a command is received, a task is scheduled for later execution,
because a command cannot preempt the currently running task. The command
returns immediately to the calling component; at a later time, an event will signal
completion to the calling component. Thus, a command does not cause a preemption
in the called component and does not cause blocking in the calling component.

## Slide 36: Components -- Events
Events in TinyOS may be tied either directly or indirectly to hardware events
Lowest-level software components interface directly to hardware interrupts
    May be external interrupts, timer events, or counter events
An event handler in a lowest-level component may handle the interrupt itself or may propagate event messages up through the component hierarchy
A command can post a task that will signal an event in the future
    In this case there is no tie of any kind to a hardware event
Notes: Events in TinyOS may be tied either directly or indirectly to hardware events.
The lowest–level software components interface directly to hardware interrupts,
which may be external interrupts, timer events, or counter events. An event handler in
a lowest-level component may handle the interrupt itself or may propagate event messages
up through the component hierarchy. A command can post a task that will signal
an event in the future. In this case, there is no tie of any kind to a hardware event.

## Slide 37
Notes: Components are organized into configurations by “wiring” them together at
their interfaces and equating the interfaces of the configuration with some of the interfaces
of the components. A simple example is shown in Figure 13.9b . The uppercase
C stands for Component. It is used to distinguish between an interface (e.g., Timer)
and a component that provides the interface (e.g., TimerC).The uppercase M stands
for Module. This naming convention is used when a single logical component has both
a configuration and a module. The TimerC component, providing the Timer interface,
is a configuration that links its implementation (TimerM) to Clock and LED providers.
Otherwise, any user of TimerC would have to explicitly wire its subcomponents.

## Slide 38: TinyOS Scheduler
Operates across all components
Only one task executes at a time
The scheduler is a separate component
    It is the one portion of TinyOS that must be present in any system
Default scheduler is a simple FIFO queue
Scheduler is power aware
  Puts processor to sleep when there is no task in the queue
Notes: The TinyOS scheduler operates across all components. Virtually all embedded systems
using TinyOS will be uniprocessor systems, so that only one task among all
the tasks in all the components may execute at a time. The scheduler is a separate
component. It is the one portion of TinyOS that must be present in any system.
The default scheduler in TinyOS is a simple FIFO (first-in-first-out) queue. A task
is posted to the scheduler (place in the queue) either as a result of an event, which triggers
the posting, or as a result of a specific request by a running task to schedule another
task. The scheduler is power aware. This means that the scheduler puts the processor to
sleep when there are no tasks in the queue. The peripherals remain operating, so that
one of them can wake up the system by means of a hardware event signaled to a lowest level
component. Once the queue is empty, another task can be scheduled only as a
result of a direct hardware event. This behavior enables efficient battery usage.
The scheduler has gone through two generations. In TinyOS 1.x, there is a shared
task queue for all tasks, and a component can post a task to the scheduler multiple
times. If the task queue is full, the post operation fails. Experience with networking
stacks showed this to be problematic, as the task might signal completion of a splitphase
operation: If the post fails, the component above might block forever, waiting
for the completion event. In TinyOS 2.x, every task has its own reserved slot in the
task queue, and a task can only be posted once. A post fails if and only if the task has
already been posted. If a component needs to post a task multiple times, it can set
an internal state variable so that when the task executes, it reposts itself. This slight
change in semantics greatly simplifies a lot of component code. Rather than test to
see if a task is posted already before posting it, a component can just post the task.
Components do not have to try to recover from failed posts and retry. The cost is one
byte of state per task.
A user can replace the default scheduler with one that uses a different
dispatching scheme, such as a priority-based scheme or a deadline scheme. However,
preemption and time slicing should not be used because of the overhead such systems
generate. More importantly, they violate the TinyOS concurrency model, which
assumes tasks do not preempt each other.

## Slide 39
Notes: Figure 13.10 shows a configuration assembled from software and hardware components.
This simplified example, called Surge and described in [GAY03], performs periodic sensor sampling and
uses ad-hoc multihop routing over the wireless network
to deliver samples to the base station. The upper part of the figure shows the
components of Surge (represented by boxes) and the interfaces by which they are
wired (represented by arrowed lines). The SurgeM component is the application level
component that orchestrates the operation of the configuration.
Figure 13.10b shows a portion of the configuration for the Surge application.
This example illustrates the strength of the TinyOS approach. The software is
organized as an interconnected set of simple modules, each of which defines one or
a few tasks. Components have simple, standardized interfaces to other components,
be they hardware or software. Thus, components can easily be replaced. Components
can be hardware or software, with a boundary change not visible to the application
programmer.

## Slide 40: TinyOS Resource Interface
TinyOS provides a simple but powerful set of conventions for dealing with resources
Dedicated
A resource that a subsystem needs exclusive access to at all times
No sharing policy is needed
Examples include interrupts and counters
Virtualized
Every client of a virtualized resource interacts with it as if it were a dedicated resource
An example is a clock or timer
Shared
Abstraction that provides access to a dedicated resource through an arbiter component
Arbiter determines which client has access to the resource at which time
Notes: TinyOS provides a simple but powerful set of conventions for dealing with resources.
Three abstractions for resources are used in TinyOS:
• Dedicated: A resource that a subsystem needs exclusive access to at all times. In
this class of resources, no sharing policy is needed since only a single component
ever requires use of the resource. Examples of dedicated abstractions include
interrupts and counters.
• Virtualized: Every client of a virtualized resource interacts with it as if it were a
dedicated resource, with all virtualized instances being multiplexed on top of a
single underlying resource. The virtualized abstraction may be used when the
underlying resource need not be protected by mutual exclusion. An example
is a clock or timer.
• Shared: The shared resource abstraction provides access to a dedicated
resource through an arbiter component. The arbiter enforces mutual exclusion,
allowing only one user (called a client) at a time to have access to a resource
and enabling the client to lock the resource.
In the remainder of this subsection, we briefly define the shared resource
facility of TinyOS. The arbiter determines which client has access to the resource
at which time. While a client holds a resource, it has complete and unfettered control.
Arbiters assume that clients are cooperative, only acquiring the resource when
needed and holding on to it no longer than necessary. Clients explicitly release
resources: There is no way for an arbiter to forcibly reclaim it.

## Slide 41
Notes: Figure 13.11 shows a simplified view of the shared resource configuration used to
provide access to an underlying resource. Associated with each resource to be shared
is an arbiter component. The arbiter enforces a policy that enables a client to lock
the resource, use it, and then release the resource. The shared resource configuration
provides the following interfaces to a client:
• Resource: The client issues a request at this interface, requesting access to the
resource. If the resource is currently locked, the arbiter places the request in a
queue. When a client is finished with the resource, it issues a release command
at this interface.
• Resource requested: This is similar to the Resource interface. In this case, the
client is able to hold on to a resource until the client is notified that someone
else needs the resource.
• Resource configure: This interface allows a resource to be automatically
configured just before a client is granted access to it. Components providing
the ResourceConfigure interface use the interfaces provided by an underlying
dedicated resource to configure it into one of its desired modes of
operation.
• Resource-specific interfaces: Once a client has access to a resource, it uses
resource-specific interfaces to exchange data and control information with the
resource.
In addition to the dedicated resource, the shared resource configuration consists
of two components. The Arbiter accepts requests for access and configuration
from a client and enforces the lock on the underlying resource. The shared resource
component mediates data exchange between the client and the underlying resource.
Arbiter information passed from the arbiter to the shared resource component controls
the access of the client to the underlying resource.

## Slide 42: Summary
Embedded systems
  Embedded system concepts
  Application versus dedicated processors
  Microprocessors
  Microcontrollers
  Deeply embedded systems
Characteristics of embedded operating systems
  Host and target environments
  Development approaches
  Adapting an existing commercial operating system
  Purpose-built embedded operating system
Embedded Linux
  Characteristics of an embedded Linux system
  Embedded Linux file systems
  Advantages of embedded Linux
  𝜇Clinux
  Android
TinyOS
  Wireless sensor networks
  TinyOS goals
  TinyOS components
  TinyOS scheduler
  TinyOS resource interface
Notes: Chapter 13 Summary